## Slide 1
01 Foundation (Chapter 1)
This chapter describes applications and their requirements to set the stage for the rest of the material.
Computer Networks: A Systems Approach, 5e
Larry L. Peterson and Bruce S. Davie
Copyright © 2010, Elsevier Inc. All rights Reserved

## Slide 2: Outline
Applications
Requirements
Network Architectures
Performance Metrics
Internet History
Socket Programming

## Slide 3: Applications
Most people know about the Internet (a computer network) through applications
  World Wide Web
  Email
  Online Social Network
  Streaming Audio Video
  File Sharing
  Instant Messaging
  …

## Slide 4: “Fun” Internet Appliances
IP picture frame
http://www.ceiva.com/
Web-enabled toaster +
weather forecaster
Internet phones
Internet
refrigerator
Slingbox: watch,
control cable TV remotely
Tweet-a-watt:
monitor energy use

## Slide 5: Application Protocol
URL
  Uniform resource locater
  http://www.cs.princeton.edu/~llp/index.html
HTTP
  Hyper Text Transfer Protocol
TCP
  Transmission Control Protocol
17 messages for one URL request
  6 to find the IP (Internet Protocol) address
  3 for connection establishment of TCP
  4 for HTTP request and reply
    Request: I got your request and I will send the data
    Reply: Here is the data you requested; I got the data
  4 messages for tearing down TCP connection

## Slide 6: Multi-Level Tasks
Application Programmer
  List the services that his application needs: delay bounded delivery of data
Network Designer
  Design a cost-effective network with sharable resources
Network Provider
  List the characteristics of a system that is easy to manage

## Slide 7: Internet structure: network of networks
End systems connect to Internet via access ISPs (Internet Service Providers)
  Residential, company and university ISPs
Access ISPs in turn must be interconnected.
  So that any two hosts can send packets to each other
Resulting network of networks is very complex
  Evolution was driven by economics and national policies
Let’s take a stepwise approach to describe current Internet structure

## Slide 8: Internet structure: network of networks
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…

## Slide 9: Internet structure: network of networks
Option: connect each access ISP to every other access ISP?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
…
…
…
…
…
connecting each access ISP to each other directly doesn’t scale: O(N2) connections.

## Slide 10: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Option: connect each access ISP to a global transit ISP? Customer and provider ISPs have economic agreement.
global ISP

## Slide 11
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors ….
ISP B
ISP A
ISP C
Internet structure: network of networks

## Slide 12
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors …. which must be interconnected
ISP B
ISP A
ISP C
IXP
IXP
peering link
Internet exchange point
Internet structure: network of networks

## Slide 13
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and regional networks may arise to connect access nets to ISPS
ISP B
ISP A
ISP C
IXP
IXP
regional net
Internet structure: network of networks

## Slide 14
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and content provider networks (e.g., Google, Microsoft, Akamai) may run their own network, to bring services, content close to end users
ISP B
ISP A
ISP B
IXP
IXP
regional net
Content provider network
Internet structure: network of networks

## Slide 15
at center: small # of well-connected large networks
  “tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider network (e.g, Google): private network that connects it data centers to Internet, often bypassing tier-1, regional ISPs
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
Regional ISP
Regional ISP
IXP
IXP
Tier 1 ISP
Tier 1 ISP
Google
IXP
Internet structure: network of networks

## Slide 16: Tier-1 ISP: e.g., Sprint
…
to/from customers
peering
to/from backbone
…
…
…
…
POP: point-of-presence

## Slide 17: Connectivity
Need to understand the following terminologies
  Link
  Nodes
  Point-to-point
  Multiple access
  Switched Network
    Circuit Switched
    Packet Switched
  Packet, message
  Store-and-forward
Point-to-point
Multiple access

## Slide 18: Connectivity
Terminologies (contd.)
  Cloud
  Hosts
  Switches
  internetwork
  Router/gateway
  Host-to-host connectivity
  Address
  Routing
  Unicast/broadcast/multicast
A switched network
Interconnection of networks
(a)
(b)

## Slide 19: Cost-Effective Resource Sharing
Resource: links and nodes
How to share a link?
  Multiplexing
  Eg. Time/Frequency-division Multiplexing, Statistical Multiplexing
Multiplexing multiple logical flows over a single physical link

## Slide 20: Resource Sharing: Circuit Switching
FDM
frequency
time
TDM
frequency
time
4 users
Example:

## Slide 21: Cost-Effective Resource Sharing
Statistical Multiplexing
  Data is transmitted based on demand of each flow.
  What is a flow?
  Packets vs. Messages
  FIFO, Round-Robin, Priorities (Quality-of-Service (QoS))
  Congested?
LAN, MAN, WAN
A switch multiplexing packets from multiple sources onto one shared link

## Slide 22: Support for Common Services
Logical Channels
  Application-to-Application communication path or a pipe
Process communicating over an abstract channel

## Slide 23: Common Communication Patterns
Client/Server
Two types of communication channel
  Request/Reply Channels
  Message Stream Channels

## Slide 24: Practical Issues - Reliability
Bits are lost
  Bit errors (1 to a 0, and vice versa)
  Burst errors – several consecutive errors
Packets are lost (congestion)
Links and Node failures
Messages are delayed
Messages are delivered out-of-order
Third parties eavesdrop
Network should hide the errors

## Slide 25: What’s a protocol?
human protocols:
“Excuse me?”
“I have a question”
introductions
… specific msgs sent
… specific actions taken when msgs received, or other events
network protocols:
machines rather than humans
all communication activity in Internet governed by protocols
protocols define format, semantics, order of msgs sent and received among network entities, and actions taken on msg transmission, receipt

## Slide 26
a human protocol and a computer network protocol:
Q: other human protocols?
Hi
Hi
Got the
time?
2:00
TCP connection
response
Get http://www.awl.com/kurose-ross
<file>
time
TCP connection
request
What’s a protocol?

## Slide 27: Protocols
Protocol defines the interfaces between the layers in the same system and with the layers of peer system
Building blocks of a network architecture
Each protocol object has two different interfaces
  service interface: operations on this protocol
  peer-to-peer interface: messages exchanged with peer
Term “protocol” is overloaded
  specification of peer-to-peer interface
  module that implements this interface

## Slide 28: Interfaces
Service and Peer Interfaces

## Slide 29: Protocols
Protocol Specification: prose, pseudo-code, state transition diagram
Interoperable: when two or more protocols that implement the specification accurately
Internet standards
  IETF: Internet Engineering Task Force
  RFC: Request For Comments

## Slide 30: Protocol Graph
Example of a protocol graph
nodes are the protocols and links the “depends-on” relation

## Slide 31: OSI Architecture
The OSI 7-layer Model
OSI – Open Systems Interconnection

## Slide 32: Internet protocol stack
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.11 (WiFi), PPP
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 33: ISO/OSI reference model
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
session: synchronization, checkpointing, recovery of data exchange
Internet stack “missing” these layers!
  these services, if needed, must be implemented in application
  needed?
application
presentation
session
transport
network
link
physical

## Slide 34: Internet Architecture
Internet Protocol Graph

## Slide 35: Internet Architecture
Defined by IETF
Three main features
  Does not imply strict layering. The application is free to bypass the defined transport layers and to directly use IP or other underlying networks
  An hour-glass shape, IP serves as the focal point for the architecture
  In order for a new protocol to be officially included in the architecture, there needs to be both a protocol specification and at least one (and preferably two) representative implementations of the specification

## Slide 36: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 37: Packet-switching: store-and-forward
takes L/R seconds to transmit (push out) L-bit packet into link at R bps
store and forward: entire packet must arrive at router before it can be transmitted on next link
one-hop numerical example:
L = 7.5 Mbits
R = 1.5 Mbps
one-hop transmission delay = 5 sec
more on delay shortly …
source
R bps
destination
1
2
3
L bits
per packet
R bps
end-end delay = 2L/R (assuming zero propagation delay)

## Slide 38: Packet Switching: queueing delay, loss
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for output link
queuing and loss:
If arrival rate (in bits) to link exceeds transmission rate of link for a period of time:
  packets will queue, wait to be transmitted on link
  packets can be dropped (lost) if memory (buffer) fills up

## Slide 39: Two key network-core functions
forwarding: move packets from router’s input to appropriate router output
routing: determines source-destination route taken by packets
  routing algorithms
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
1
2
3
0111
dest address in arriving
packet’s header

## Slide 40: Alternative : circuit switching
end-end resources allocated to, reserved for “call” between source & dest:
In diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
circuit segment idle if not used by call (no sharing)
Commonly used in traditional telephone networks

## Slide 41: Circuit switching: FDM vs.TDM
FDM
frequency
time
TDM
frequency
time
4 users
Example:
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 42: Packet switching vs. circuit switching
example:
1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active at same time is less than .0004
packet switching allows more users to use network!
N
users
1 Mbps link
Q: how did we get value 0.0004?
Q: what happens if > 35 users ?
…..

## Slide 43: Packet switching vs. circuit switching
great for bursty data
  resource sharing
  simpler, no call setup
excessive congestion possible: packet delay and loss
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior?
  bandwidth guarantees needed for audio/video apps
  still an unsolved problem
is packet switching a “slam dunk winner?”
Q: human analogies of reserved resources (circuit switching) versus on-demand allocation (packet-switching)?

## Slide 44: Performance Metrics
Delay
Bandwidth
Loss
Delay = Propagation + Transmit + Queue + Processing
  Propagation = distance/speed of light
  Transmit = size/bandwidth
One bit transmission => propagation is important
Large bytes transmission => bandwidth is important

## Slide 45: How do loss and delay occur?
packets queue in router buffers
packet arrival rate to link (temporarily) exceeds output link capacity
packets queue, wait for turn
A
B
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 46: Four sources of packet delay
dproc: nodal processing
check bit errors
determine output link
typically < msec
A
B
propagation
transmission
nodal
processing
queueing
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
dnodal = dproc + dqueue + dtrans + dprop

## Slide 47
dtrans: transmission delay:
L: packet length (bits)
R: link bandwidth (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed in medium (~2x108 m/sec)
dprop = d/s
dtrans and dprop
very different
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
Four sources of packet delay
Notes: 47

## Slide 48: Bandwidth
Bandwidth
  Width of the frequency band
  Number of bits per second that can be transmitted over a communication link
1 Mbps: 1 x 106 bits/second ~= 1x220 bits/sec
1 x 10-6 seconds to transmit each bit or imagine that a timeline, now each bit occupies 1 micro second space.
On a 2 Mbps link the width is 0.5 micro second.
Smaller the width more will be transmission per unit time.

## Slide 49: Bandwidth
Bits transmitted at a particular bandwidth can be regarded as having some width:
(a) bits transmitted at 1Mbps (each bit 1 μs wide);
(b) bits transmitted at 2Mbps (each bit 0.5 μs wide).

## Slide 50: Delay X Bandwidth
We think the channel between a pair of processes as a hollow pipe
Latency (delay) length of the pipe and bandwidth the width of the pipe
Delay of 50 ms and bandwidth of 45 Mbps
50 x 10-3 seconds x 45 x 106 bits/second
2.25 x 106 bits = 280 KB data.
Network as a pipe

## Slide 51: Delay X Bandwidth
Relative importance of bandwidth and latency depends on application
  For large file transfer, bandwidth is critical
  For small messages (HTTP, NFS, etc.), latency is critical
  Variance in latency (jitter) can also affect some applications (e.g., audio/video conferencing)

## Slide 52: Delay X Bandwidth
  How many bits the sender must transmit before the first bit arrives at the receiver if the sender keeps the pipe full
  Takes another one-way latency to receive a response from the receiver
  If the sender does not fill the pipe—send a whole delay × bandwidth product’s worth of data before it stops to wait for a signal—the sender will not fully utilize the network

## Slide 53: Delay X Bandwidth
Infinite bandwidth
  RTT dominates
  Throughput = TransferSize / TransferTime
  TransferTime = RTT + 1/Bandwidth x TransferSize
Its all relative
  1-MB file to 1-Gbps link looks like a 1-KB packet to 1-Mbps link

## Slide 54: Relationship between bandwidth and latency
A 1-MB file would fill the 1-Mbps link 80 times,
but only fill the 1-Gbps link 1/12 of one time

## Slide 55: Internet history
1961: Kleinrock - queueing theory shows effectiveness of packet-switching
1964: Baran - packet-switching in military nets
1967: ARPAnet conceived by Advanced Research Projects Agency
1969: first ARPAnet node operational
1972:
  ARPAnet public demo
  NCP (Network Control Protocol) first host-host protocol
  first e-mail program
  ARPAnet has 15 nodes
1961-1972: Early packet-switching principles
Notes: https://www.youtube.com/watch?v=2d7sPPlefok

## Slide 56
1970: ALOHAnet satellite network in Hawaii
1974: Cerf and Kahn - architecture for interconnecting networks
1976: Ethernet at Xerox PARC
late70’s: proprietary architectures: DECnet, SNA, XNA
late 70’s: switching fixed length packets (ATM precursor)
1979: ARPAnet has 200 nodes
Cerf and Kahn’s internetworking principles:
  minimalism, autonomy - no internal changes required to interconnect networks
  best effort service model
  stateless routers
  decentralized control
define today’s Internet architecture
1972-1980: Internetworking, new and proprietary nets
Internet history

## Slide 57
1983: deployment of TCP/IP
1982: smtp e-mail protocol defined
1983: DNS defined for name-to-IP-address translation
1985: ftp protocol defined
1988: TCP congestion control
new national networks: Csnet, BITnet, NSFnet, Minitel
100,000 hosts connected to confederation of networks
1980-1990: new protocols, a proliferation of networks
Internet history

## Slide 58
early 1990’s: ARPAnet decommissioned
1991: NSF lifts restrictions on commercial use of NSFnet (decommissioned, 1995)
early 1990s: Web
  hypertext [Bush 1945, Nelson 1960’s]
  HTML, HTTP: Berners-Lee
  1994: Mosaic, later Netscape
  late 1990’s: commercialization of the Web
late 1990’s – 2000’s:
more killer apps: instant messaging, P2P file sharing
network security to forefront
est. 50 million host, 100 million+ users
backbone links running at Gbps
1990, 2000’s: commercialization, the Web, new apps
Internet history

## Slide 59
2005-present
~750 million hosts
  Smartphones and tablets
Aggressive deployment of broadband access
Increasing ubiquity of high-speed wireless access
Emergence of online social networks:
  Facebook: soon one billion users
Service providers (Google, Microsoft) create their own networks
  Bypass Internet, providing “instantaneous” access to search, email, etc.
E-commerce, universities, enterprises running their services in “cloud” (eg, Amazon EC2)
Internet history

## Slide 60: Application Programming Interface
Interface exported by the network
Since most network protocols are implemented (those in the high protocol stack) in software and nearly all computer systems implement their network protocols as part of the operating system, when we refer to the interface “exported by the network”, we are generally referring to the interface that the OS provides to its networking subsystem
The interface is called the network Application Programming Interface (API)

## Slide 61: Application Programming Interface (Sockets)
Socket Interface was originally provided by the Berkeley distribution of Unix
  - Now supported in virtually all operating systems
Each protocol provides a certain set of services, and the API provides a syntax by which those services can be invoked in this particular OS

## Slide 62: Socket
What is a socket?
  The point where a local application process attaches to the network
  An interface between an application and the network
  An application creates the socket
The interface defines operations for
  Creating a socket
  Attaching a socket to the network
  Sending and receiving messages through the socket
  Closing the socket

## Slide 63: Socket
Socket Family
  PF_INET denotes the Internet family
  PF_UNIX denotes the Unix pipe facility
  PF_PACKET denotes direct access to the network interface (i.e., it bypasses the TCP/IP protocol stack)
Socket Type
  SOCK_STREAM is used to denote a byte stream
  SOCK_DGRAM is an alternative that denotes a message oriented service, such as that provided by UDP

## Slide 64: Creating a Socket
int sockfd = socket(address_family, type, protocol);
The socket number returned is the socket descriptor for the newly created socket
int sockfd = socket (PF_INET, SOCK_STREAM, 0);
int sockfd = socket (PF_INET, SOCK_DGRAM, 0);
The combination of PF_INET and SOCK_STREAM implies TCP

## Slide 65: Client-Serve Model with TCP
Server
  Passive open
  Prepares to accept connection, does not actually establish a connection
Server invokes
int bind (int socket, struct sockaddr *address,
int addr_len)
int listen (int socket, int backlog)
int accept (int socket, struct sockaddr *address,
int *addr_len)

## Slide 66: Client-Serve Model with TCP
Bind
  Binds the newly created socket to the specified address i.e. the network address of the local participant (the server)
  Address is a data structure which combines IP and port
Listen
  Defines how many connections can be pending on the specified socket

## Slide 67: Client-Server Model with TCP
Accept
  Carries out the passive open
  Blocking operation
    Does not return until a remote participant has established a connection
    When it does, it returns a new socket that corresponds to the new established connection and the address argument contains the remote participant’s address

## Slide 68: Client-Serve Model with TCP
Client
  Application performs active open
  It says who it wants to communicate with
Client invokes
int connect (int socket, struct sockaddr *address,
int addr_len)
Connect
  Does not return until TCP has successfully established a connection at which application is free to begin sending data
  Address contains remote machine’s address

## Slide 69: Client-Serve Model with TCP
In practice
  The client usually specifies only remote participant’s address and let’s the system fill in the local information
  Whereas a server usually listens for messages on a well-known port
  A client does not care which port it uses for itself, the OS simply selects an unused one

## Slide 70: Client-Serve Model with TCP
Once a connection is established, the application process invokes two operation
int send (int socket, char *msg, int msg_len,
int flags)
int recv (int socket, char *buff, int buff_len,
int flags)

## Slide 71: Example Application: Client
#include <stdio.h>
#include <sys/types.h>
#include <sys/socket.h>
#include <netinet/in.h>
#include <netdb.h>
#define SERVER_PORT 5432
#define MAX_LINE 256
int main(int argc, char * argv[])
{
FILE *fp;
struct hostent *hp;
struct sockaddr_in sin;
char *host;
char buf[MAX_LINE];
int s;
int len;
if (argc==2) {
host = argv[1];
}
else {
fprintf(stderr, "usage: simplex-talk host\n");
exit(1);
}

## Slide 72: Example Application: Client
/* translate host name into peer’s IP address */
hp = gethostbyname(host);
if (!hp) {
fprintf(stderr, "simplex-talk: unknown host: %s\n", host);
exit(1);
}
/* build address data structure */
bzero((char *)&sin, sizeof(sin));
sin.sin_family = AF_INET;
bcopy(hp->h_addr, (char *)&sin.sin_addr, hp->h_length);
sin.sin_port = htons(SERVER_PORT);
/* active open */
if ((s = socket(PF_INET, SOCK_STREAM, 0)) < 0) {
perror("simplex-talk: socket");
exit(1);
}
if (connect(s, (struct sockaddr *)&sin, sizeof(sin)) < 0) {
perror("simplex-talk: connect");
close(s);
exit(1);
}
/* main loop: get and send lines of text */
while (fgets(buf, sizeof(buf), stdin)) {
buf[MAX_LINE-1] = ’\0’;
len = strlen(buf) + 1;
send(s, buf, len, 0);
}
}

## Slide 73: Example Application: Server
#include <stdio.h>
#include <sys/types.h>
#include <sys/socket.h>
#include <netinet/in.h>
#include <netdb.h>
#define SERVER_PORT 5432
#define MAX_PENDING 5
#define MAX_LINE 256
int main()
{
struct sockaddr_in sin;
char buf[MAX_LINE];
int len;
int s, new_s;
/* build address data structure */
bzero((char *)&sin, sizeof(sin));
sin.sin_family = AF_INET;
sin.sin_addr.s_addr = INADDR_ANY;
sin.sin_port = htons(SERVER_PORT);
/* setup passive open */
if ((s = socket(PF_INET, SOCK_STREAM, 0)) < 0) {
perror("simplex-talk: socket");
exit(1);
}

## Slide 74: Example Application: Server
if ((bind(s, (struct sockaddr *)&sin, sizeof(sin))) < 0) {
perror("simplex-talk: bind");
exit(1);
}
listen(s, MAX_PENDING);
/* wait for connection, then receive and print text */
while(1) {
if ((new_s = accept(s, (struct sockaddr *)&sin, &len)) < 0) {
perror("simplex-talk: accept");
exit(1);
}
while (len = recv(new_s, buf, sizeof(buf), 0))
fputs(buf, stdout);
close(new_s);
}
}

## Slide 75: Summary
Applications
Expectation/Requirements from a computer network
Layered architecture for computer network
Performance metrics
Brief History
Socket interface and programming