## Slide 1: Data Communication Components over Physical Layer
Data
  Analog: Continuous value data (sound, light, temperature)
  Digital: Discrete value (text, integers, symbols)
Signal
  Analog: Continuously varying electromagnetic wave
  Digital: Series of voltage pulses (square wave)
Transmission
  Analog: Works the same for analog or digital signals
  Digital: Used only with digital signals

## Slide 2: Analog vs. Digital Signals
Analog signals have a continuously varying voltage-versus-time graph

## Slide 3: Analog vs. Digital Signals
Digital signals have a square wave with instant transitions from low to high voltage states (0 to 1)

## Slide 4: Bit Rate, Bit Length, Baud rate
Bit Rate
  The number of bits sent in 1 second
  Unit: bps
Bit Length
  The distance one bit occupies on the transmission medium
  Unit: meter, micro meter, nano meter, etc.
  Propagation speed x bit duration
Baud Rate
  The number of signals sent in 1 second
  Bit rate = Baud rate x n ( where n is the number of bits per signal)

## Slide 5: Transmission Impairment
Attenuation:
  The decrease in magnitude of a signal as it travels through a transmission medium
Distortion:
  Any undesired change in a signal during transmission (e.g. out of phase)
Noise:
  An undesirable signal due to low-quality of a transmission medium, impeding the true signal

## Slide 6
Figure 3.26 Attenuation

## Slide 7
Figure 3.29 Noise

## Slide 8: Signal-to-Noise (SNR) Ratio
SNR = Average Signal Power/Average Noise Power
SNRdB = 10 log10 SNR

## Slide 9: Two Important Results on data rate, capacity:
Nyquist Theorem for a noiseless channel
  Gives maximum theoretical bit rate
Shannon’s Law for a noisy channel
  Gives an estimate on capacity

## Slide 10: Bandwidth: two usage of the term
“analog” world: bandwidth in Hz
  refers to range of frequencies (=high-low)
“digital” world: bandwidth in bits/sec
  Refers to speed of bit transmission in a link
Nyquist & Shannon’s results gives us a rough idea on how to go between these two terms (noiseless/noise)
  However, it doesn't’t tell us what coding was used (to be discussed later)

## Slide 11: Nyquist’s Theorem
Aka the Sampling Theorem
D = 2B log2 L
(D: Data rate, B: Bandwidth, L: signal levels)
If the sampling rate is less than 2xmax_freq, some of the highest frequency components in the analog input signal will not be correctly represented in the digitized output.

## Slide 12: Shannon’s Law of a noisy channel
Noisy means the channel has noise; thus, need to incorporate signal-to-noise in estimating capacity
The capacity of a channel
  = bandwidth x log2 (1 + SNR)

## Slide 13
Consider a channel with a 1-MHz bandwidth. The SNR for this channel is 63. What are the appropriate bit rate and signal level?
Example: Combining Shannon & Nyquist
For better performance choose something lower, 4 Mbps, for example. Thus, use the Nyquist formula to find the number of signal levels.
Solution
First, we use the Shannon formula to find the upper limit.
The Shannon capacity gives us the upper limit; the Nyquist formula tells us how many signal levels we need.

## Slide 14
If the available channel is a bandpass channel, we cannot send the digital signal directly to the channel; we need to convert the digital signal to an analog signal before transmission.
Note

## Slide 15
Figure 3.24 Modulation of a digital signal for transmission on a bandpass channel

## Slide 16
Convert the following into the Frequency-domain representation

## Slide 17: Digital Transmission
Digital-To-Digital Conversion
Analog-To-Digital Conversion

## Slide 18: Analog Data-->Signal Options
Analog data to analog signal
  Easy conversion (eg telephone)
  Used in traditional analog telephony
Analog data to digital signal
  Requires a codec (encoder/decoder)
  Allows use of digital telephony, voice mail

## Slide 19: Digital Data-->Signal Options
Digital data to analog signal
  Requires modem (modulator/demodulator)
  Necessary when analog transmission is used
Digital data to digital signal
  Less expensive when large amounts of data are involved
  More reliable because no conversion is involved

## Slide 20: Digital-to-digital Conversion
Line Coding: digital data to digital signals
Block Coding: mB/nB coding (optionally used)
Scrambling: to avoid long 0s (optionally used)

## Slide 21
Figure 4.1 Line coding and decoding

## Slide 22
Figure 4.2 Signal element versus data element

## Slide 23: Issues on Digital Transmission
Self-synchronization.
  Clock skew between sender and receiver
Built-in error detection.
Immunity to Noise.
Complexity.
  Needs time to interpret (2 levels vs. 64 levels)
Baseline Wandering.
  In decoding digital signal, a running average (baseline) is used to evaluate the incoming signal power. Long 0s make the baseline down.
  DC components

## Slide 24
Figure 4.3 Effect of lack of synchronization

## Slide 25
Figure 4.4 Line coding schemes

## Slide 26
Figure 4.7 Polar RZ scheme

## Slide 27
Figure 4.6 Polar NRZ-L and NRZ-I schemes

## Slide 28
Figure 4.8 Polar biphase: Manchester and differential Manchester schemes

## Slide 29
Bipolar schemes: Alternate Mark Inversion (AMI) and pseudoternary
Used by T1 with scrambling

## Slide 30
Figure 4.19 Two cases of B8ZS scrambling technique
B8ZS substitutes eight consecutive zeros with 000VB0VB.

## Slide 31: Analog-To-digital Conversion
Pulse Code Modulation (PCM)
Delta Modulation (DM)

## Slide 32
Figure 4.21 Components of PCM encoder

## Slide 33
Figure 4.22 Three different sampling methods for PCM

## Slide 34
Figure 4.24 Recovery of a sampled sine wave for different sampling rates
According to the Nyquist theorem, the sampling rate must be
at least 2 times the highest frequency contained in the signal.

## Slide 35
Figure 4.26 Quantization and encoding of a sampled signal

## Slide 36
Figure 4.27 Components of a PCM decoder

## Slide 37
We want to digitize the human voice. What is the bit rate, assuming 8 bits per sample?
Solution
The human voice normally contains frequencies from 0 to 4000 Hz. So the sampling rate and bit rate are calculated as follows:
Example 4.14

## Slide 38
Figure 4.28 The process of delta modulation

## Slide 39: Analog Transmission
Digital-To-Analog Conversion
Analog-To-Analog Conversion

## Slide 40: Digital-To-Analog Conversion

## Slide 41
Figure 5.6 FSK

## Slide 42
Figure 5.3 ASK

## Slide 43
Figure 5.10 Implementation of BPSK

## Slide 44
Figure 5.8 PSK

## Slide 45
Figure 5.12 Concept of a constellation diagram

## Slide 46
Figure 5.9 PSK constellation

## Slide 47
Figure 5.11 The 4-PSK characteristics

## Slide 48
Figure 5.10 The 4-PSK method

## Slide 49
Figure 5.14 The 4-QAM and 8-QAM constellations

## Slide 50
Figure 5.15 Time domain for an 8-QAM signal

## Slide 51
Figure 5.16 16-QAM constellations

## Slide 52
Figure 5.17 Bit and baud

## Slide 53
Figure 5.14 The 4-QAM and 8-QAM constellations

## Slide 54
Figure 5.15 Time domain for an 8-QAM signal

## Slide 55
Figure 5.16 16-QAM constellations

## Slide 56
Figure 5.17 Bit and baud

## Slide 57: Analog-To-Analog Conversion

## Slide 58
Figure 5.24 Analog-to-analog modulation

## Slide 59
Figure 5.26 Amplitude modulation

## Slide 60
Frequency modulation (FM)

## Slide 61
Phase Modulation (PM)
Notes: Unlike its more popular counterpart, frequency modulation (FM), PM is not very widely used for radio transmissions.
This is because it tends to require more complex receiving hardware and there can be ambiguity problems in determining whether, for example, the signal has changed phase by +180° or -180°.
PM is used, however, in digital music synthesizers
ASK. Simple and cheap
FFSK. Reliable and very good BER
PSK has a higher speed but perhaps is more difficult adjustment if you are using links between your different stations.

## Slide 62
Figure 5.19 Modulation/demodulation

## Slide 63
Figure 7.18 Propagation methods

## Slide 64
Figure 7.19 Wireless transmission waves

## Slide 65
Figure 7.17 Electromagnetic spectrum for wireless communication
1 GHz

## Slide 66: Summary
Digital data to digital signal
  Line coding
    RZ, NRZ, Machester, AMI, …
  Block coding: mB/nB
  Scrambling: B8ZS, …
Analog data to digital signal
  PCM, DM
Digital data to analog signal
  ASK, FSK, PSK, QAM
Analog data to analog signal
  AM, FM, PM